## Slide 1
MappView for EFI
Jorge Murria 27/Oct/2020

## Slide 2
Introduction
Visualization technology in B&R PLC
  Multi-Client/Multi-user
  Based in OPC UA
    Fast, security, events
  Web based technology
    Based in Identifyers
  Integrated HELP in AS gives a lot of information
http://localhost:81/index.html
2

## Slide 3
Topologies
3

## Slide 4
Structure of application
MappView folder in Logical
  Full application definition
App definition in Configuration
  Running events and bindings
  XML files
4

## Slide 5
Elements of HMI (1)
5
Contents
Widget
Compound
Widget
Dropdown
ImageList
PushButton
NumericInput
NumericOutput
Button
Image
Area
Page

## Slide 6
Elements of HMI (2)
6

## Slide 7
Elements of HMI (3)
7
Page → Layout
  A Layout contain Areas
        Sizes and positions
  Area contains a Content
    Widgets
    Labels, Images, etc

## Slide 8
Elements of HMI (3.1)
8

## Slide 9
Widgets (1)
9

## Slide 10
Widgets (2)
10
All the configuration in Properties
Possible select more than 1 object
  Texts definition
        Direct
        From Texts file
  Image/media definition
        From resources

## Slide 11
Compound Widgets (1)
11
Already created an EFIWidgetLib
The CompoundWidget do not have graphical
Defined a DevelopContent to create the Content
  Copy the widgets from DevelopContent & Define the mapping

## Slide 12
Bindings
Relation between widgets and data
  Specific for each configuration
  Enabled in the configuration of the application
  Read, write, read/write
XML file, plain text
12

## Slide 13
EventBindings
Actions to do after an event
  Specific for each configuration
  Enabled in the configuration of the application
  Source –> Handler –> Action –> Target
13

## Slide 14
Texts
Defined in Resources/Texts/PageTexts.txm
  Languages defined in the project
  Namespace IAT (cannot be changed)
    Assignation: $IAT/TextID; Sample:$IAT/Mach.Reset;
14

## Slide 15
Units
Search the desired unit in Code for Units.xls
  Define the Unit in the widget
  Input the value in the orange column
15

## Slide 16
OPC UA (1)
The server is define per Configuration
  Config→ Connectivity→ OpcUA→ OpcUaMap.uad
  Global variables & Program Variables
Users in AccessAndSecurity
  Users and roles
Permissions defined in server variables
16

## Slide 17
OPC UA (2)
17

## Slide 18
Sample in Automation Studio
Sample when installing version
  Unzip file in destination
  Open project
  Review sample
18

## Slide 19
Programming rules.1
All identifyers MUST finish with the type
The identifier -->FileName_ElementType
  _Page _Layout
  _Content _Dialog
  _Binding
  _EventBinding
19

## Slide 20
Programming rules.2
All binding files MUST be reformatted before committing to repository
  Using Notepad++
  XML Tools plugin
  Pretty Print [Ctrl+Alt+Shift+B]
20

## Slide 21
Programming rules.3
Diagnosis page to visualize directly PLC cards
  Using Compound widgets
  Add Compound widgets if necessary
21

## Slide 22
Programming rules.4
Enable OpcUa structures in Automatic Mode
  Work with permissions
  Reduce maintenance of code in server
22

## Slide 23
Programming rules.5
Texts and alarms stored in csv file
  Define code, text and variable to raise alarm
    Automatically created texts indexes
    Automatically created alarms code
    Indexed can be used from widgets
23